## Slide 1
DESIGN OF STATE MACHINE USING VHDL/XILINX
PREPARED BY- 1.
2.
3.
4.

## Slide 2: Sequential logic implementation
Sequential circuits
  primitive sequential elements (Flip-Flops)
  combinational logic
Models for representing sequential circuits
  finite-state machines (Moore and Mealy)
  representation of memory (states)
  changes in state (transitions)
Basic sequential circuits
  shift registers
  counters
Design procedure
  state diagrams
  state transition table
  next state functions

## Slide 3: State machine model
Values stored in registers are the state of the circuit
Combinational logic computes:
  next state
  outputs
    function of current state and inputs (Mealy machine)
    function of current state only (Moore machine)
Inputs
Outputs
Next State
Current State
output logic
next state logic

## Slide 4: State Machine Model
States: S1, S2, ..., Sk
Inputs: I1, I2, ..., Im
Outputs: O1, O2, ..., On
Transition function: Fs(Si, Ij)
Output function: Fo(Si) or Fo(Si, Ij)
Inputs
Outputs
Next State
Current State
output logic
next state logic
Clock
Next State
State
0
1
2
3
4
5

## Slide 5: How do we turn a state diagram into logic?
e.g. counter
  flip-flops to hold state
  logic to compute next state
  clock signal controls when flip-flop memory can change
    wait just long enough for combinational logic to compute new value
D
Q
D
Q
D
Q
OUT1
OUT2
OUT3
CLK
"1"

## Slide 6: FSM design procedure
Describe FSM behavior, e.g. state diagram
  Inputs and Outputs
  States (symbolic)
  State transitions
State diagram to state transition table, i.e. truth table
  Inputs: inputs and current state
  Outputs: outputs and next state
State encoding
  decide on representation of states
  lots of choices
Implementation
  flip-flop for each state bit
  synthesize combinational logic from encoded state table

## Slide 7: Synthesis Example
Present State Next State
C B A C+ B+ A+
0 0 0 x x x
0 0 1 x x x
0 1 0 1 0 1
0 1 1 1 1 0
1 0 0 0 1 0
1 0 1 0 1 1
1 1 0 1 0 0
1 1 1 x x x
note the don't care conditions that arise from the unused state codes
Implement simple count sequence: 000, 010, 011, 101, 110
Derive the state transition table from the state transition diagram
101
010
100
110
011

## Slide 8: Mealy vs. Moore Machines
Moore: outputs depend on current state only
Mealy: outputs may depend on current state and current inputs
A
L’ R’ / TR, F
L / TL
L’ R / TL, F

## Slide 9: Specifying outputs for a Moore machine
D/1
E/1
B/0
A/0
C/0
1
0
0
0
0
1
1
1
1
0
reset
current next reset input state state output
1 – – A
0 0 A B 0
0 1 A C 0
0 0 B B 0
0 1 B D 0
0 0 C E 0
0 1 C C 0
0 0 D E 1
0 1 D C 1
0 0 E B 1
0 1 E D 1
Output is only function of state
  specify in state bubble in state diagram
  Example (what does it do?)

## Slide 10: Specifying outputs for a Mealy machine
current next reset input state state output
1 – – A 0
0 0 A B 0
0 1 A C 0
0 0 B B 0
0 1 B C 1
0 0 C B 1
0 1 C C 0
B
A
C
0/1
0/0
0/0
1/1
1/0
1/0
reset/0
Output is function of state and inputs
  specify output on transition arc between states

## Slide 11: Comparison of Mealy and Moore machines
state feedback
inputs
outputs
reg
combinational logic for next state
logic for outputs
inputs
outputs
state feedback
reg
combinational logic for next state
logic for outputs
Mealy machines tend to have fewer states
  different outputs on arcs (i*n) rather than states (n)
Mealy machines react faster to inputs
  react in same cycle – don't need to wait for clock
  delay to output depends on arrival of input
Moore machines are generally safer to use
  outputs change at clock edge (always one cycle later)
  in Mealy machines, input change can cause output change as soon as logic is done – a big problem when two machines are interconnected – asynchronous feedback

## Slide 12: DEMUX USING MEALY MACHINE
DEMUX is a combinational circuit that routes one input to various channels depending on the states. The states are defined by user in terms of binary input that is regulated by the type of DEMUX, for example the 2 X 4 DEMUX depends on 2 states and routes the output in 4 different outputs. In the above diagram, the states have values in the form of INPUT/OUTPUT, for example – input of S0 state is 00 and output is 0 and it goes back to its own state as shown in the diagram.
Analyzing the mealy circuit, we can say that it depends on both the output and next state. The output will change multiple times even for the same state depending upon the input. In a DEMUX the output is fixed and it cannot be changed with respect to the states, changing states can regulate output on different ports or channel but the value cannot be changed. So, a mealy circuit cannot be used to implement a DEMUX.

## Slide 13: DEMUX USING MOORE MACHINE
In Moore circuit, the output is dependent only on the next state and not on the output. They have a fixed output per state. The state has a stable output as shown in S0 has 0 and S1 has 1. In the consideration of DEMUX, the output is required to be fixed instead of depending on the inputs.
Current State | Next State |  | Output
 | Input = 00 | Input = 01 | 
S0 | S0 | S1 | 0
S1 | S1 | S1 | 1

## Slide 14
DESIGN OF STATE MACHINE USING VHDL/XILINX
THANK YOU 